## Slide 1: Expanding into VHF … and beyond!
10 Sept 2022
Randy Wing, N0LD
636-459-0964
N0LD@arrl.net

## Slide 2: Stations that Heard us on 2m
N0LD/R – Randy, Harvey KB0YHT/R - Nick
Mt. Scott – EM04
70 miles SE of Wichita, KS – EM17
September 2021 VHF Contest

## Slide 3: Do I need mucho $$$? No!
KB0YHT/R’s setup included:
  Used Yaesu FT-100 (160m through 70cm all-mode radio)
  2m/70cm mag-mount vertical – on the side of his car- horizontal
  6m vertical – on the side of his car - horizontal
Band openings happen all the time – but how often? - I’ll get to that!
VHF Contests happen occasionally – but how often? - I’ll get to that!
Modest Expenses – Extraordinary Results!
Key Factors

## Slide 4: What Do you mean “expand” into VHF … and beyond?
VHF Definition
Why VHF?
Where can I take this?
Advanced Topics
Operate “beyond” what you do today! Stretch yourself!

## Slide 5: VHF Definition
VHF extends from 30 mhz to 300 mhz which includes:
    6 m 50-54 Mhz
    2 m 144-148 Mhz
    1.25 m 222-225 Mhz
UHF extends from 300 mhz to 3 ghz which includes:
    70 cm 420-450 Mhz
    33 cm 902-928 MHZ
    23 cm 1240-1300 Mhz
    13 cm 2300-2310 MHZ and 2390-2450 MHZ
“Microwave” is what hams call the bands above UHF (sometimes above 1 Ghz
    5 cm 5650-5925 MHZ
    3 cm 10 – 10.5 Ghz
    Many more … including light!
This isn’t a test!

## Slide 6: WHy VHF?
VHF is an entry into Amateur Radio – almost everyone has a 2m handheld!
VHF has so many avenues to explore!
  FM Repeaters -> FM Simplex -> Other modes!
  VHF Contesting (FM only, Participation, Competing, Setting Records)
  APRS – good way to tell when there are VHF openings
  Meteor Skip
  Amateur Satellite communication (FM -> USB/LSB -> Digital)
    International Space Station Communication
  Moon Bounce
Extend your range – extend your fun!
Are you Curious? This is what VHF is about!

## Slide 7: VHF and Height - FM
The higher the antenna the better for VHF
At a glance this seems obvious, but how high do I need my antenna?
Buildings and hills block VHF Signals (mostly)
Vegetation is a minor impedance on VHF; major impedance on UHF+
As you start, get your antennas above your house, then the trees, then higher
If you are mobile, seek out the peak of hills
If you are buying land, buy a house on a hill, without HOAs, in the country!
FM Simplex requires an antenna above a house; Above trees for real gain
Above a house is ~7 miles range; if you are on a hill ~30 miles!

## Slide 8: VHF and Height - USB
Same as FM, but because of the mode the range is greater on USB/Digital
Although there are some who FM-DX; An opening is best realized on USB/Digital
VHF Propagation and Scatter affects range dramatically in USB/Digital stations
Need your Horizontal antenna above the trees and as high as you can get it!
If rovering, look for hills or watertowers for high land!
At Ground level on the island - Who can talk farther to the North? FM or USB on 2m? – Height is better

## Slide 9: Advanced Topics
Satellites
Meteor Scatter
EME
VHF POTA
VHF Contesting

## Slide 10: Satellites!
Randy Wing, N0LD

## Slide 11: Affordable, Challenging Satellite operation
“National Parks on The Air - Satellite Activation #2 - Blue Ridge Parkway – YouTube”
The first time you see someone use Satellites to make a ham radio contact:
  What just happened!
  I had not idea I could do that!
  Wow! I want to try that!
  What do I need to buy to try that?
Why operate satellites?
  Rewards small efforts to improve
  Rapidly improves your operating skills
  Guaranteed to make your neighbors wonder about you!

## Slide 12: Affordable, Challenging Satellite operation
See attached Amateur-Radio-Satellites-V1.pdf

## Slide 13: K5ND, Jim Wilson Satellite Briefing
See attached Amateur-Radio-Satellites-V1.pdf

## Slide 25: S.A.T. by CSN
Just purchased
Easy to Install / Integrate
Affordable ~$250

## Slide 26: Meteor Scatter
Randy Wing, N0LD

## Slide 27: Meteor Scatter Introduction
“10 Meter Meteor Scatter QSO - YouTube”
Similar to 6m FT8, just use the MSK144 mode
  WSJT or any digital program with MSK144
  You can make verbal qsos / CW qsos on 6m – if you are fast!
Why operate meteor scatter?
  Easy - most months have a meteor shower that can result in contacts
  Easy - If you can operate WSJT-X, you can do meteor scatter!
  Rewarding - Paper chasing – FFMA, 6m VUCC, 2m VUCC. Etc.

## Slide 28: How and When Meteor Scatter Works
G0ISW Meteor Scatter (qsl.net)
Get on the “rocks”!

## Slide 29: Meteor Scatter What do I need? Why Should I?
“10 Meter Meteor Scatter QSO - YouTube”
Similar to 6m FT8, just use the MSK144 mode
  WSJT or any digital program with MSK144
  You can make verbal qsos / CW qsos on 6m – if you are fast!
What do I need?
  Radio capable of VHF all mode operation – preferably 6m, then more
  6m Loop or even a dipole M2 6m Loop – gain helps
  You can try other bands, 2m is popular, people experiment on 1.25m and 70cm
Why operate meteor scatter?
  Easy - most months have a meteor shower that can result in contacts
  Easy - If you can operate WSJT-X, you can do meteor scatter!
  Rewarding - Paper chasing – FFMA, 6m VUCC, 2m VUCC. Etc.

## Slide 30: EME
Randy Wing, N0LD

## Slide 31: EME – the Challenge!
Portable EME moon bounce setup – YouTube
If you setup a sked with a large station EME you can operate moonbounce with a 12 ft 70cm antenna, 100 watts, and WSJT-X using the JT65 mode
More antennas in tandem vastly improves performance!
More power vastly improves performance!

## Slide 32: Typical EME Stations

## Slide 33: Closeup

## Slide 34: VHF POTA
Credit to Marcus Sutliff, N5ZY
Full story on: Parks on the Air – N5ZY (https://n5zy.org/parks-on-the-air)

## Slide 35: OK POTA – N5ZY
20-Aug 2022: My first park activation, K-0493, GRID EM04 Wichita Mountains Wildlife Refuge & Mt Scott Project

## Slide 36: Deployed N5ZY Rover
On the air with 2m and 6m Moxons from PAR Electronics
Omniangle Antennas | PAR Electronics | loop | vhf uhf loop antenna | weak signal HO loop

## Slide 37: Inside the Rover

## Slide 38: N5ZY VHF Operating Conditions

## Slide 39: Construction Many details on the N5ZY website (aforementioned)
Design rules:
Read your vehicle’s roof rack load limit!
It’s not how fast you can drive, it’s how fast you can stop with everything still attached. Most cars use friction clamps for the roof rack and in an emergency stop you may overcome the friction holding them on! Go lightly, and keep as much weight as low as possible.
Remember that if something comes loose it could kill someone. Be mindful of safety and inspect at every opportunity.
Do not drink and drive because then using it as a jousting rod may seem like a great idea.
Do not have two horizontal masts as they could resemble blasters and invite Imperial stormtroopers to attack.
The mast is an MFJ-1906H. (Note: DXE-TCFP-33HD is a new Carbon Fiber version of the same thing! This wasn’t available in July!) The tilt base is the DXE-VA-BASE I also added the wing nut knobs, DXE-AOK-TB1193

## Slide 40: VHF Contest Fun!
Randy Wing, N0LD

## Slide 41: What is VHF Contesting?
Competing with other Amateur Radio VHF operators
Weak Signal / Horizontally polarized antennas
Higher Power the better / but many use “barefoot” power
Using 50 mhz and above frequencies
Popular VHF contests:
  ARRL Spring Sprints (50 144, 222, 432, 902 and up)
  ARRL January, June, and September VHF Contests
  CQ World Wide VHF Contest (15-16 July 2017)
Fixed, Rover, Multi-Op Categories
  Fixed: SOHP, SOLP, SO Portable, SO 3-Band (50, 144, 432 mhz), SO FM Only
  Rover: Rover, Classic Rover, Limited Rover (lowest 4 bands), Unlimited Rover
  Multi-Op: MO Limited (max 4 bands), Multi-operator Unlimited

## Slide 42: Why are you here?
I would like you to consider trying VHF contesting!
VHF Contesting is increasing! ~10% increase in June 2017
Midwest and southern Plains have a lot of flat terrain! Conducive to VHF
We need more VHF contest operators to have more fun!
…and most importantly…

## Slide 43: VHF Contesting is Fun!
Challenge:
  Compete with others in your “contest class”
  Can do it alone or with others
Excitement:
  Band Openings – during contests they are more noticeable!
  Helping Friends, Making Friends
  Learning – Opportunities to Mentor and be Mentored
Awards:
  Recognition from the contest sponsor; VHF contests are collaborative as well as competitive
Side Benefits:
  Improves operating skills
  Excellent preparation for emergency operations
  An excellent use of our allocated spectrum Remember: “Use it or lose it.”

## Slide 44: Grid Squares
Grid Squares are:
  2 deg EW; 1 deg NS
  ~100 miles x 60 miles
Example: Ardmore, OK
  EM14 “Echo Mike , One Four”
  Please copy …N0LD/R in EM14
Strategy
  Go North and South thru corners as much as possible (60 miles < 100 miles)
  Stay within VHF population center range
o Ardmore, OK
o Dodge City, KS

## Slide 45: How Do You Score in a VHF Contest?
QSO Points (read the rules they change)
Count 1 point for each 50- or 144-MHz QSO
Count 2 points for each 222- or 432-MHz QSO
Count 3 points for each 902- or 1296-MHz QSO *
Count 4 points for each 2.3 GHz (or higher) QSO *
TIP - Work Mode that is quickest (or that you can)
Multipliers
    Total number of different grid squares worked per band
Final Score
    Total QSO Points x Total Multipliers = Final Score
* January VHF and other contests has different points

## Slide 46: Propagation
http://aprs.mountainlake.k12.mn.us/

## Slide 47: Propagation
http://www.dxmaps.com/spots/mapg.php?Lan=E&Frec=MUF&ML=M&HF=N

## Slide 48: Propagation
http://www.dxinfocentre.com/tropo.html

## Slide 49: What do I need to start?
Recommend a small 6m Beam and a 2m Beam ~ $200 each
Recommend a used radio such as FT-100, FT-857D < $600

## Slide 50: Where do I go from here?
Recommend a 70cm gain antenna ~ $230 each
Recommend a 2m amplifier (85W) < $160

## Slide 51: Fixed Operation Antenna Examples
No matter what size station you’re operating, it’s a thrill to talk to somebody far away.

## Slide 52: Fixed Operation Antenna Examples (more)
You’ll improve your VHF operation – just START!

## Slide 53: Do I Have to Have a “Contest Station”?
Big Gun contest stations
  Multiple radios
  Multiple towers
  Serious station automation
Small Gun – Big Fun stations
  There are opportunities for “guest operating” if you have a big gun nearby!
  Ask your club members to all get on the air on 146.52 FM!
  If there isn’t anyone on, right now – try again several times later!
    Band conditions change things!
You don’t have to be a Big Gun to have Big Fun contesting!

## Slide 54: Who enters a contest? Why?
The Casual Contester
  A desire to just have some fun, improve operating skills, and work new countries, states, counties, etc. from the smorgasbord of participating stations
The Feisty Contester
  A desire to compete
  … individually, or as part of a club.
The Committed Contester
  Able to leap tall buildings with a single bound
  Able to master the art of sleep deprivation
CQ Contest!
Contesting can be like this sometimes!

## Slide 55: How to Win a Contest
Choose the “Class” to match your goals!
  Limited, Unlimited, Rover (classic, limited, unlimited), Single-Op, Multi-Op, LP/HP
Work a lot of stations
Work as many “multipliers” as possible
Work smart
  Make email/telephone contacts with potential contacts – get the word out!
  Make good band change decisions
  Use efficient operating techniques
    Don’t waste time or words (similar to emergency operations)
    Know when to “Run” and when to “Search & Pounce”
    Know when to take a break

## Slide 56: N0LD/R and K5SRT/R Team Up! (cont.)
Tactics!
  Used all the bands that we have radios for!
    N0LD/R already had 6m, 2m, 1.25m, 70cm, & 23 cm - added 33cm Alinco FM handheld
    K5SRT/R already had 6m, 2m, 1.25m, 70cm – added 33cm and 23 cm FM handhelds
  Used as many antennas as we could come up
    N0LD/R
      6m Loop, 2m and 70cm dual loops, 2m / 70cm vertical - added 33cm vertical ($8!)
      2m, 1.25m, 70cm, 23cm – 10 ft long yagis - added 33cm beam (7 ft long – 80$)
    K5SRT/R
      2m, 70cm verticals - added 6m and 33cm vertical – used 23cm adapted radio rubber antenna
      2m, 1.25m, and 70cm loops - added 6m loop ($180)
      2m (3 elements), 70cm (5 elements)
  TIP – During contest what is the best radio and antenna? The one that’s used

## Slide 57: K5SRT/R Configuration
For September 2018 ARRL VHF Contest

## Slide 58: K5SRT/R - Antenna and Radios Diagram

## Slide 59: K5SRT/R Sept. 2018 Rover Hill Top
2M/70cm Vertical x2
33M Vertical Stub
23M Vertical Rubber Duck
70 cm Loop
2M Loop
1.25M Loop
6M Loop
2M Yagi
70 cm Yagi
70cm Vertical Flag Pole
23M Vertical Stub
*2M/70cm Vertical (Front Left Not Seen)
6M Vertical Ham Stick

## Slide 60: K5SRT/R Equipment, Tips, & Notes
Remain flexible - Things change!
  Not everything goes the way you plan: Light vs dark, good vs bad weather, equipment operational/no operational, propagation open/closed, team may need a break, frequency or equipment interference
  Take notes/Build a list of things to improve on the next trip
Monitor, give calls, and share contacts and frequencies with others
  VHF Contesting is friendly and collaborative – keep the spirit going! Elmer!
Work where people are (FM simplex, SSB, Digital, and antenna type)
  FM Simplex is a great way to pick people up – and it is OK to solicit people on local repeaters!
Be helpful and encourage others
  everyone can learn something or improve
Start coax installs from the operators perspective
  Store excess coax and equipment spares outside of the operators position

## Slide 61: K5SRT/R Equipment, Tips, & Notes
Start Planning Early!
  We start planning at least two months before a contest!
  Have plans, do test runs, have maps (electronic and paper), alternate routes and use visual aids for operational awareness (helpful during a Grid Dance)
  Build checklists for installation, beginning the contest, Grid Dancing, and supplies
  Consider this rover as the practice run for your next!
Communicate clearly so that your logger can be accurate
  Don’t go faster than they can log; no need to make the loggers life miserable!
Change position
  Let the other people in your car drive, operate, log – it will improve everyone’s enjoyment
Capture and document before, during, and after the event
  Your antenna configuration, your coax, your switches, your power, everything!
  Capture your configuration in pictures as well

## Slide 62: Visual Operator Aid & Remain Flexible
Add additional antenna options, test & verify your configuration
EM26
EM25
MAPS

## Slide 63: K5SRT/R Electrical Power Diagram

## Slide 64: K5SRT/R Power Diagram Notes
Alternator & Battery (source and connections)
Safety fuses for protecting wiring and equipment
AC & DC (Four Position) Master Power Switch
  Off, AC Only, DC Only, Both AC & DC
  Added LED red lights to enable awareness if equipment is powered
Use what you have and improve things based on a plan.
  Son gave me a 1500 Watt Inverter, N0LD loaned some equipment
Look for flexible things
  AC Power Strip has 2- USB ports in addition to outlets for PCs this also free up vehicle power points
Anderson Power Poles or standardized installation connections
  Allows you to add or change components easily
  Allows you to add a team member at the last minute that has additional equipment
Watch for interference, loose power, and ground connections

## Slide 65: N0LD/R External Rover Setup
For September 2018 ARRL VHF Contest

## Slide 66: N0LD/R
6m Loop
70cm Dual Loops
2m Dual Loops
70cm Yagi
2m Yagi
1.25m Yagi
23cm Yagi
33 cm Yagi
33 cm Yagi
2M/70cm Vertical
33M Vertical

## Slide 67: Focus on the Loops
Nom.
Yagi Range
Nom. Loop Range
70cm Dual Loops
2M Dual Loops
6M Loop

## Slide 68: N0LD/R Internal Rover Setup
September 2018

## Slide 69
2m / 70cm Vertical
Dual 2m Loops
2m Beam
6m Loop
Dual 70cm Loops
70cm Beam
1.25m Beam
33cm Vertical
33cm Beam
23cm Beam
150 W 2m Amp
100 W 70 cm Amp
2m Switch
70 cm Switch
33 cm Switch
Power Meter
Yaesu
FT-736R
Yaesu
FT-847
Kenwood
TM-D710A
Alinco
DJ-G29T
N0LD/R RF Architecture
30 Aug 2018
Power Meter
Power Meter

## Slide 70
2m / 70cm Vertical
Dual 2m Loops
2m Beam
6m Loop
Dual 70cm Loops
70cm Beam
1.25m Beam
33cm Vertical
33cm Beam
23cm Beam
150 W 2m Amp
100 W 70 cm Amp
2m Switch
70 cm Switch
33 cm Switch
Power Meter
Yaesu
FT-736R
Yaesu
FT-847
Kenwood
TM-D710A
Alinco
DJ-G29T
N0LD/R RF and Power Architecture
Dual
Powr Switch
Car Battery
40 Amp Dist.
40 Amp Dist.
Voltage Upconv.
Voltage Upconv.
Power Meter
Power Meter

## Slide 71: Lego Shelves

## Slide 72: AB0RX at the N0LD/R main operating position

## Slide 73
Yaesu FT-847
Yaesu FT-736r
70cm amp – 100 watts
2m amp – 200 watts
2m and 70cm Watt meters
6m Watt meter
Digital for 6m
WinUSB for CW
1.25m amp – 100 watts
Switches for 2m, 70cm, and 33 cm (hidden)
Power Switch
Power Voltage Up-converters & Dual Distribution Switches

## Slide 74
ICOM 9700
Yaesu FT-736r
Front seat for 1.25m
2m Digital
6m Digital Laptop
AC Power
Logging Laptop – customer software by KG9DUK
Switches for 2m, 70cm, and 33 cm (hidden)
Power Switch
ICOM 7610 for 6m
W0HGJ, Harvey

## Slide 75: W0HGJ – FM and 6m Digital Operation

## Slide 76: Laptop harness over seat back

## Slide 77: Station 3 – FM 2m & 70cm
Pre-loaded with Repeater Frequencies specific to the rover trip
Kenwood TM-D710 radio

## Slide 78: N0LD/R and K5SRT/R On The Road
September 2018

## Slide 79: N0LD/R and K5SRT/R Team Up!
How can we expand the number of VHF Rovers?
  Find interested people; take them for a ride!
  We’ve grown from N0LD to N0LD/KC0MTM to N0LD/KB0YHT to N0LD/KB0YHT/K5SRT to
  … this September’s dual rover team
Strategy – how did we win a VHF award for Rover?
  There are three categories of VHF Rover entries:
    Classic – up to 2 people; limits on QSOs w/ rovers of 100;
    Limited – up to 2 people; limits on QSOs w/ rovers of 100; only 6m thru 70cm; limited power
    Unlimited – any # of people; no limits, unlimited power
Best For Our Teams
Unlimited is not popular; not seen as true competition
To win at Unlimited – you have to “gang up” in teams!

## Slide 80: N0LD/R and K5SRT/R Team Up! (cont.)
Tactics!
  Built an almost 400 person deep VHF location database
    Used our prior contest logs
    Used the logs of friendly fixed based stations
    Asked everyone for their operational status (bands, phone #, email address)
    Determine their latitude / longitude from QRZ
    Constantly under upgrade for current status
  From this - determined the VHF population centers locations

## Slide 81: Developed a VHF Database
Over 250 HF hams currently in our database
Grayed squares allows cutting and pasting to Hamstermap.com
Copy grayed columns to Hamstermap.com

## Slide 82: Grid Square Visualization Tool #1
http://hamstermap.com/custommap.html
Copy and replace this information with the grayed columns from the previous page

## Slide 83: Grid Square Visualization Tool #2
https://k7fry.com/grid/

## Slide 84: County Visualization Tool
https://www.randymajors.com/p/countygmap.html
Or Google Maps!

## Slide 85: VHF Stations
Black circles are amateur radio VHF stations with 2m and 70cm and who have been active within the last 5 years
Red circles are more active amateur radio VHF stations with 2m and 70cm and 6m
Green crosses are VHF super stations – active and multiple bands
White pluses are the edges of the grid squares

## Slide 86: N0LD/R and K5SRT/R Team Up! (cont.)
Tactics!
  Focused on Grid “Circling” in eastern KS and OK; started in western KS
  Plot a route close to the grid circles
    As close to North and South as possible
    Then prepare detailed full route planning:
      At each grid square
      And between the grid squares
    Include operational action queues so that new and experienced operators know

## Slide 88: Grid Square Visualization Tool #2
http://qthlocator.free.fr/index.php?locator=EM12
and
“snipping tool”

## Slide 89: Grid Square Visualization Tool #3
http://dxcluster.ha8tks.hu/hamgeocoding/
and
“snipping tool”
Dynamically calculates lat, long, and grid as you move your mouse from location to location !!!
A
B
C
D

## Slide 90
Itinerary
Depart Nick’s House @ Noon on 7 Sep, 2018
Arrive Woodward for rest stop @ 2:30 PM
Arrive @ Dodge House Hotel & Convention Center, 2408 W Wyatt Earp Blvd, Dodge City @ 5 PM
EM05
EM15
EM16
EM06
DM95
DM96
EM17
EM07
DM97
EM18
EM08
DM98

## Slide 91: N0LD/R and K5SRT/R On The Road
September 2018

## Slide 92: Good Morning, Dodge City, KS!

## Slide 93
Itinerary – Saturday Sept 8 Morning
Sleep in until 7:30 AM; Have breakfast at 8:00 AM in the hotel or anywhere
Check out 8:45 AM
Tour local Boot Hill Museum at 500 W Wyatt Earp Blvd, Dodge City, KS 67801 from 9 AM through 11:30 AM; Depart Museum
Pick up fast food on the way out of town – one last restroom break!
Head east on US Highway 283
DodgeHouse
BootHill
Wright
DM97
EM07

## Slide 94
Itinerary – Saturday Sept 8 Morning (cont)
Continue North on US Highway 283
Turn left (west) at the Jetmore Airport on F Rd
Proceed 4 miles to the west to the starting point for the contest – Point 97E in DM97!
Establish IM for N0LD/R
Arrive about Noon
Recommend calling and trying to work before 1 PM:
DM97
EM07
E
Wright
Jetmore
 | Callsign | telephone | Grid | 6m | 2m | 1.25m | 70cm | 33cm | 23cm | 13cm
 | K0BJ | 785-462-0884 | DM99kj | Y | Y |  |  |  |  | 
 | K0RCJ | 620-755-4826 | EM18ei | Y | Y |  | Y |  |  | 
 | K5ZG | 419-230-1827 | DM88 | Y | Y |  |  |  |  | 
 | KB0ZOM | 406-740-2114 | EN00tn | Y | Y | Y | Y |  |  | 
 | KF0M | 316-617-3133 | EM17io | Y | Y | Y | Y |  | Y | 
 | N0KQX | 620-521-0464 | DM97nx | y | Y |  | Y |  | Y | 
 | N0KQY | N0KQY@wbsnet.org | DM98gk | y | Y | Y | Y |  | Y | 
 | N0LL | 785-282-5831 | EM09os | y | Y | Y | Y |  |  | 
 | N0YK | 620-874-2292 | DM98ml | Y | Y | Y | Y |  | Y | 
 | W3DHJ | w3dhj@jonz.net | DM78rf | Y | Y |  | Y |  |  | 
 | W5AFY | 972-839-6992 | EM04id | Y | Y | Y | Y | Y | Y | Y
 | WQ0P | 785-213-7072 | EM19wf | Y | Y | Y | Y | Y | Y | Y

## Slide 95
  Stations we might reach from western Kansas
N0KQX
N0YK
N0KQY
WA0VJR
K5ZG
K0BJ
KD0ARW
N0LL
KB0ZOM
AE0G
WQ0P
WA0ARM
KF0M
K0RCJ
DM98
EM08
DM97
EM07
DM99
EM09
DN90
EN00
DN80
DM89
DM88
DM87
EM18
EM17
EM19
EN10
E
F
D
H
I
G
KD0EZS
W3DHJ
KC3OL

## Slide 96
Itinerary – Point E (SW of Jetmore, KS)
Recommend contacting N0LL, WQ0P, W3HDJ, N0YK, K5ZG, KB0ZOM, KC3OL, KD0ARW, KF0M, K0RCJ, N0KQX, N0KQY, K0BJ
N0LD/R to work locals during transition and hand off each local & band to K5SRT/R
08E
DM98
EM08
DM97
EM07
97E
07E
98E
 |  |  | K5SRT/R |  | Contact?
N0LD/R | Point 97E | DM97 | Point 97E | DM97 | 
 | Point 97E | DM97 | Point 98E | DM98 | 
 | Point 97E | DM97 | Point 08E | EM08 | 
 | Point 97E | DM97 | Point 07E | EM07 | 
N0LD/R | Point 98E | DM98 | Point 07E | EM07 | 
 | Point 98E | DM98 | Point 98E | DM98 | 
 | Point 98E | DM98 | Point 08E | EM08 | 
 | Point 98E | DM98 | Point 97E | DM97 | 
N0LD/R | Point 08E | EM08 | Point 97E | DM97 | 
 | Point 08E | EM08 | Point 98E | DM98 | 
 | Point 08E | EM08 | Point 08E | EM08 | 
 | Point 08E | EM08 | Point 07E | EM07 | 
N0LD/R | Point 07E | EM07 | Point 07E | EM07 | 
 | Point 07E | EM07 | Point 98E | DM98 | 
 | Point 07E | EM07 | Point 08E | EM08 | 
 | Point 07E | EM07 | Point 97E | DM97 | 

## Slide 97: At the Start of the Contest! 1:00 PM Sat

## Slide 98: Early in the Sept VHF contest…
K3NT-Bob noted 6m SWR problem working digital while in route to next four square.
K5SRT-Ross checks for loose 6m connection on ham stick
A brief stop near Ness City, KS is also a good time for everyone to stretch legs and to capture pictures to remember events later (note the clouds).

## Slide 99
Itinerary – Transition from Point F to Point D (Part 3 of 3)
At Exit 221; Turn left (north on US-14) towards Lincoln, KS;
Recommend calling or texting 20 min before arrival:
  W5AFY – Dan - 972-839-6992
  N0LL – Larry - 785-282-5831
  WQ0P – Greg - 785-213-7072
  N0YK – Chad - 620-874-2292
  KB0ZOM – Ben - 406-740-2114
  KF0M – John - 316-617-3133
  K0RCJ - Richard-620-755-4826
  N0KQX – Dale - 620-521-0464
  K0BJ – Bruce - 785-462-0884
K5SRT/R travel 10.3 miles to E. Iron Dr.; turn right (east) onto E. Iron Dr; travel 8.3 miles east to Point 18D
N0LD/R travel 11.3 miles to E. Jaguar Dr; Turn right (east) onto E. Jaguar Dr; travel 8 miles to reach Point 09D
EM18
EM19
EM08
EM09
E. Jaguar Drive
Exit 221
E. Iron Drive
D
Jaguar
Iron
Exit221

## Slide 100: Some excitement late Saturday night…
Torrential rainfall over the last week
Western KS was not bad; just a little sloppy
As we neared Lincoln, KS – fog was forming; but no VHF opening
As we approached the grid corner… the road was very muddy
We were late two hours as we cleaned the car up so we could drive
Notes: We pressed on, because the 4 wheel drive was handling it
However, the bridge was out near the grid corner
We turned around and went south to the better road
Our detour route was bad; we lost traction, acquired a lot of clay
But we got out!

## Slide 101: This is the aftermath; New Wiper Blades!

## Slide 102: After a brief 5 hour night… we took off! South of Maple Hill, KS about 10 miles

## Slide 103
Itinerary – Transition from Point I to Point H (Part 1 of 3)
Depart Point I NLT 9:00 AM
Drive west on Blazingstar Rd to Keene-Eskridge RD
Turn left (south) on Keene-Eskridge Rd – travel 4 miles
Merge with KS-4; travel on KS-4 to Eskridge; turn left (south) on KS-99; travel 35 miles; merge with Burlingame Rd
Break stop in Emporia
Follow KS-99 through Emporia
Arrive NLT 11:00 AM at Point H
EM17
EM18
EM27
EM28
H
I

## Slide 104
Itinerary – Point H
(Virgil, KS)
Arrive 11 AM
N0LD/R: Arrive Point 17H
K5SRT/R: Arrive Point 27H
Attempt contact with everyone we made a contact with at Point I
Depart NLT 12:30 PM
17H
27H
28H
EM17
EM18
EM27
18H
EM28
 |  |  | K5SRT/R |  | Contact?
N0LD/R | Point 17H | EM17 | Point 27H | EM27 | 
 | Point 17H | EM17 | Point 17H | EM17 | 
 | Point 17H | EM17 | Point 18H | EM18 | 
 | Point 17H | EM17 | Point 28H | EM28 | 
N0LD/R | Point 18H | EM18 | Point 28H | EM28 | x
 | Point 18H | EM18 | Point 18H | EM18 | x
 | Point 18H | EM18 | Point 17H | EM17 | 
 | Point 18H | EM18 | Point 27H | EM27 | 
N0LD/R | Point 28H | EM28 | Point 27H | EM27 | 
 | Point 28H | EM28 | Point 17H | EM17 | 
 | Point 28H | EM28 | Point 18H | EM18 | x
 | Point 28H | EM28 | Point 28H | EM28 | x
N0LD/R | Point 27H | EM27 | Point 28H | EM28 | 
 | Point 27H | EM27 | Point 18H | EM18 | 
 | Point 27H | EM27 | Point 17H | EM17 | 
 | Point 27H | EM27 | Point 27H | EM27 | 

## Slide 105: EM17 (17H) - Near Virgil, KS

## Slide 106: 27H - East of Virgil, KS

## Slide 107
Itinerary – Point G (West of Caney, KS)
Arrive 2:30 PM
N0LD/R: Arrive Point 26G
K5SRT/R: Arrive Point 17G
Attempt contact with everyone we made a contact with at Point H and the people who answered the phone call
Depart NLT 4 PM
16G
26G
27G
EM16
EM17
EM26
17G
EM27
 |  |  | N0LD/R |  | Contact?
K5SRT/R | Point 17G | EM17 | Point 17G | EM17 | x
 | Point 17G | EM17 | Point 27G | EM27 | x
 | Point 17G | EM17 | Point 26G | EM26 | 
 | Point 17G | EM17 | Point 16G | EM16 | 
K5SRT/R | Point 27G | EM27 | Point 16G | EM16 | 
 | Point 27G | EM27 | Point 26G | EM26 | 
 | Point 27G | EM27 | Point 27G | EM27 | x
 | Point 27G | EM27 | Point 17G | EM17 | x
K5SRT/R | Point 26G | EM26 | Point 17G | EM17 | 
 | Point 26G | EM26 | Point 27G | EM27 | 
 | Point 26G | EM26 | Point 26G | EM26 | 
 | Point 26G | EM26 | Point 16G | EM16 | 
K5SRT/R | Point 16G | EM16 | Point 16G | EM16 | 
 | Point 16G | EM16 | Point 26G | EM26 | 
 | Point 16G | EM16 | Point 27G | EM27 | 
 | Point 16G | EM16 | Point 17G | EM17 | 

## Slide 108
  Stations we might reach from eastern Oklahoma
N5AFY
WD5AGO
N5GEX
KB0HH
N0MUA
K5CFY
K5SW
EM26
EM25
EM27
EM16
EM17
EM17
O
G
L
B
N0MST
K5LAD
KD5AFS
K5CM
K5WE
KB5MR
N5OSK
N5NET

## Slide 109
EM16
EM26
O
Itinerary – Transition from Point G to O (Part 2 of 2)
West of Owasso:
  Contact Owasso and Tulsa repeaters
  Status Facebook and check position reporting website
Crossing into EM16:
  Contact Tulsa repeaters
  Contact Sapulpa repeaters
Arrive NLT 5:30 PM at Point O
Turkey Mountain is a high bluff over the Tulsa area

## Slide 110
Itinerary – Point O (Tulsa, OK)
Traverse Outside Points
Traverse Inner Points
Traverse Inner Points for other rovers
Depart NLT 7:15 PM for Edmond OK
15O1
25O
26O
16O
EM16
EM26
EM15
EM25
E1390 Rd, Lamar, OK 74850
25O1
26O1
16O1
 |  |  | K5SRT/R |  | Contact?
N0LD/R | Point 26O | EM26 | Point 26O | EM26 | x
 | Point 16O | EM16 | Point 16O | EM16 | x
 | Point 15O1 | EM15 | Point 15O1 | EM15 | 
 | Point 25O | EM25 | Point 25O | EM25 | 
 |  |  | K5SRT/R |  | Contact?
N0LD/R | Point 25O1 | EM25 | Point 25O1 | EM25 | 
 | Point 25O1 | EM25 | Point 15O1 | EM15 | 
 | Point 25O1 | EM25 | Point 16O1 | EM16 | 
 | Point 25O1 | EM25 | Point 26O1 | EM26 | 
N0LD/R | Point 15O1 | EM15 | Point 26O1 | EM26 | 
 | Point 15O1 | EM15 | Point 25O1 | EM25 | 
 | Point 15O1 | EM15 | Point 15O1 | EM15 | 
 | Point 15O1 | EM15 | Point 16O1 | EM16 | 
N0LD/R | Point 16O1 | EM16 | Point 16O1 | EM16 | 
 | Point 16O1 | EM16 | Point 26O1 | EM26 | 
 | Point 16O1 | EM16 | Point 25O1 | EM25 | 
 | Point 16O1 | EM16 | Point 15O1 | EM15 | 
N0LD/R | Point 26O1 | EM26 | Point 15O1 | EM15 | 
 | Point 26O1 | EM26 | Point 16O1 | EM16 | 
 | Point 26O1 | EM26 | Point 26O1 | EM26 | 
 | Point 26O1 | EM26 | Point 25O1 | EM25 | 

## Slide 111: Point O Inner Circle The way to make fast points rover-to-rover
15O1
EM16
EM26
EM15
EM25
25O1
26O1
16O1

## Slide 112: N3FJP Networked VHF Contesting

## Slide 113: N0LD/R Team
W0HGJ
Harvey
AB0RX
George
N0LD
Randy

## Slide 114: K5SRT/R Team
K3NT
Bob
KB0YHT
Nick
K5SRT
Ross

## Slide 115: Final Score

## Slide 116: VHF Take-Aways
Start with a decent 6m all-mode radio with modern radio interfaces
Start with a moxon or loop on 6m
Operate in the VHF contests – it is lonely without that!
Expand into 2m all-mode with modern radio interfaces
Start with a moxon or loop on 2m
Upgrade to longer Yagi antennas and rotators
Master your equipment, then try something new every 6 months or so

## Slide 117: Backup Charts
Randy Wing, N0LD

## Slide 118: A Personal Introduction
Grew up in NE Iowa on a dairy farm – interest in astronomy and technology; discovered AM dxing when given an old radio
Iowa State University – NROTC, degree in computer science
Have worked for Boeing since 1984, software/systems eng, mgmt, sales
I’ve been a ham since August 1996
Enjoy VHF and HF operation - casual contesting, Dxing, satellites, SKYWARN, exploring digital, kit building – working on microwave radios
“I cannot predict what I will like until I try it!”

## Slide 119: Calling Frequencies
Important per-band frequencies:
  Band Call Freq QSO Freq FM Freq
  6m 50.125 USB 50.145 USB 52.525 FM
  2m 144.200 USB 144.220 USB 146.52 FM
  1.25m 222.100 USB 222.120 USB 223.5 FM
  70cm 432.100 USB 432.120 USB 446 FM
  33cm 902.100 USB 902.100 USB 902.125 FM
  903.125 FM
  915.000 FM
  23cm 1296.1 USB 1296.120 USB 1294.5 FM

## Slide 120: Calling Frequencies
Important per-band frequencies:
  Band Call Freq QSO Freq FM Freq
  6m 50.125 USB 50.145 USB 52.525 FM
  2m 144.200 USB 144.220 USB 146.52 FM
  1.25m 222.100 USB 222.120 USB 223.5 FM
  70cm 432.100 USB 432.120 USB 446 FM
  33cm 902.100 USB 902.100 USB 902.125 FM
  903.125 FM
  915.000 FM
  23cm 1296.1 USB 1296.120 USB 1294.5 FM

## Slide 121: Modern Radios
FT-991A
ICOM 9700
ICOM 905
ICOM 9700
FT-991A
*** NEW – not released! ***

## Slide 122: Alinco DJ-G7T (1.25m/33cm) Radio

## Slide 123: Final Antenna Layout
2M Yagi
70cm Yagi
1.25M Yagi
23cm Yagi
2M Dual Loops
2M Vertical
70cm Vertical
70cm Dual Loops
6M Loop

## Slide 124: Current N0LD/Rover

## Slide 125: WSJT-X – 6m digital operation